## Slide 1: Extraction Thimbles

## Slide 2: What are Extraction Thimbles?
Extraction thimbles are small, tube-shaped containers designed to hold solid samples for extraction processes. They are commonly used in Soxhlet extraction apparatus, where a solvent continuously passes through the sample to extract desired compounds.
Typically made of Cellulose…
  Suitable for non-aggressive, general-purpose extraction
Or Glass..
  Suitable for use with hot, acidic or alkaline solutions
Or Quartz
  Suitable for extremely high temperatures and aggressive chemicals
Sartorius offers Cellulose grade C300 and Glass Fiber grade G400 in various sizes.

## Slide 3: Features
Temperature limit for extraction
500 °C
Different Materials
31
Natural Ingredients
100%
Toxic Additives
0%
Cellulose
24
Glass Fiber
7
Wall Thickness
1.3 for under 35 mm, 1.7 for over 35 mm
1.3 mm – 1.7 mm

## Slide 4: Core Benefits for the customer
Resistance
Accuracy
Fast Delivery
High Purity

## Slide 5: Applications
Particularly effective for measuring free lipid content in food and beverages, identifying additives in both food products and elastomers, and monitoring soil samples as well as hot air streams. In the pharmaceutical area most relevant in the extraction of active pharmaceutical ingredients (API’s).
Examination of components in natural products like vitamins and amino acids.
Determination of the fiber content in food.
Determination of free or bound fatty acids/greasy materials in foodstuffs, e.g. fat determination in accordance with Weibull-Stoldt or the AOAC International Hydrolysis Method
Analyses of pesticide waste, poly-aromatic carbohydrates and dioxins in foodstuffs by hot extraction.

## Slide 6
1
5
2
3
4
What is the shelf life?
What are temperature limits and how about reusability?
How do I prepare the timbles and what happens after the extraction?
What is the µm retention rate?
Which size and volume?
Frequently asked questions

## Slide 7: How do I find out which thimbles fits best for my extractor / target volume?
It is important that the outer diameter (=inner diameter + 2x wall thickness) of the thimble fits into the extractor with a suitable pitch. For example, an extractor with an NS 45/40 pitch (the 2nd number (40) is the inner diameter of the extractor) matches a slightly smaller inner diameter of the thimble, in this case 35mm ID. And the length of the tube should be a little higher (0.5 - 1 cm) than the overflow siphon on the main body of the extractor, but lower than the bypass that goes into the main body above the siphon.
Volume mL | Dimensions mm (ID x Height)
30 | 22 x 80
100 | 33 x 93
250 | 33 x 205
500 | 48 x 230
1000 | 57 x 315

## Slide 8: What is the shelf life for the extraction thimbles?
A Shelf Life of at least 5 years from the date of manufacturing under storage condition as follows:
Temperature : 15 - 30 °C
Relative Humidity : 40 - 60 %
Exclusion of air pollutants of any kind
No direct sunlight.

## Slide 9: What are the temperature limits for different types of thimbles?
Cellulose thimbles can withstand temperatures of up to 220 degrees Celsius, while glass fibre thimbles can withstand temperatures of up to 500 degrees Celsius.
Can the Extraction Thimbles be reused?
No, we do not recommend reusing the thimbles. Usually, the extractables of different samples are characterised. Using only one thimble for different samples can lead to cross contamination and errors in the results, as the thimbles cannot be properly cleaned in between.

## Slide 10: How do I prepare a thimble for the extraction?
No pre-treatment or pre-wetting is required. May be handled with gloves, depending on the sensitivity of the subsequent analysis. For analysis of particulate matter in exhaust gas, the thimble must be weighed before insertion into the pipe.
What happens after the target medium has been completely extracted
In most cases, the extracted substances are concentrated by evaporation for further analysis and quantification. To do this, the vessel containing the solvent and extracted substances is transferred to an evaporator system.

## Slide 11: What is the µm retention rate of thimbles used in filtration processes?
There is no defined µm retention rate. The permeability of thimbles is similar to that of very open filter papers with a high flow rate, just to retain the sample and its fragments.
Notes: No defined rate since we are talking about an irregular depth filter matrix which is not comparable to any predefined pore size of a micro- or ultrafilter.

## Slide 12
Sebastian Kamlot, Product Manager Lab Filtration
© 2024 Copyright Sartorius Lab Instruments GmbH & Co. KG, Otto-Brenner-Straße 20
37079 Göttingen, Germany
Thank You.